## Slide 1
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th Edition, Global Edition Jim Kurose, Keith Ross Pearson April 2016
Chapter 9 Multimedia Networking

## Slide 2: Multimedia networking: outline
9.1 multimedia networking applications
9.2 streaming stored video
9.3 voice-over-IP
9.4 protocols for real-time conversational applications
9.5 network support for multimedia

## Slide 3: Multimedia: audio
analog audio signal sampled at constant rate
  telephone: 8,000 samples/sec
  CD music: 44,100 samples/sec
each sample quantized, i.e., rounded
  e.g., 28=256 possible quantized values
  each quantized value represented by bits, e.g., 8 bits for 256 values
time
audio signal amplitude
analog
signal
quantized value of
analog value
quantization error
sampling rate
(N sample/sec)

## Slide 4: Multimedia: audio
example: 8,000 samples/sec, 256 quantized values: 64,000 bps
receiver converts bits back to analog signal:
  some quality reduction
example rates
CD: 1.411 Mbps
MP3: 96, 128, 160 kbps
Internet telephony: 5.3 kbps and up
time
audio signal amplitude
analog
signal
quantized value of
analog value
quantization error
sampling rate
(N sample/sec)

## Slide 5: Multimedia: video
video: sequence of images displayed at constant rate
  e.g., 24 images/sec
digital image: array of pixels
  each pixel represented by bits
coding: use redundancy within and between images to decrease # bits used to encode image
  spatial (within image)
  temporal (from one image to next)
……………………...…
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………………...…
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i

## Slide 6: Multimedia: video
……………………...…
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………………...…
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i
CBR: (constant bit rate): video encoding rate fixed
VBR: (variable bit rate): video encoding rate changes as amount of spatial, temporal coding changes
examples:
  MPEG 1 (CD-ROM) 1.5 Mbps
  MPEG2 (DVD) 3-6 Mbps
  MPEG4 (often used in Internet, < 1 Mbps)

## Slide 7: Multimedia networking: 3 application types
streaming, stored audio, video
  streaming: can begin playout before downloading entire file
  stored (at server): can transmit faster than audio/video will be rendered (implies storing/buffering at client)
  e.g., YouTube, Netflix, Hulu
conversational voice/video over IP
  interactive nature of human-to-human conversation limits delay tolerance
  e.g., Skype
streaming live audio, video
  e.g., live sporting event (futbol)

## Slide 8: Multimedia networking: outline
9.1 multimedia networking applications
9.2 streaming stored video
9.3 voice-over-IP
9.4 protocols for real-time conversational applications
9.5 network support for multimedia

## Slide 9: Streaming stored video:
video
recorded (e.g., 30 frames/sec)
2. video
sent
Cumulative data
streaming: at this time, client
playing out early part of video,
while server still sending later
part of video
network delay
(fixed in this example)
time
3. video received,
played out at client
(30 frames/sec)

## Slide 10: Streaming stored video: challenges
continuous playout constraint: once client playout begins, playback must match original timing
  … but network delays are variable (jitter), so will need client-side buffer to match playout requirements
other challenges:
  client interactivity: pause, fast-forward, rewind, jump through video
  video packets may be lost, retransmitted

## Slide 11: Streaming stored video: revisited
constant bit
rate video
transmission
Cumulative data
time
variable
network
delay
client video
reception
constant bit
rate video
playout at client
client playout
delay
buffered
video
client-side buffering and playout delay: compensate for network-added delay, delay jitter

## Slide 12: Client-side buffering, playout
variable fill
rate, x(t)
client application
buffer, size B
playout rate,
e.g., CBR r
buffer fill level, Q(t)
video server
client

## Slide 13: Client-side buffering, playout
variable fill
rate, x(t)
client application
buffer, size B
playout rate,
e.g., CBR r
buffer fill level, Q(t)
video server
client
1. Initial fill of buffer until playout begins at tp
2. playout begins at tp,
3. buffer fill level varies over time as fill rate x(t) varies and playout rate r is constant

## Slide 14: Client-side buffering, playout
playout buffering: average fill rate (x), playout rate (r):
x < r: buffer eventually empties (causing freezing of video playout until buffer again fills)
x > r: buffer will not empty, provided initial playout delay is large enough to absorb variability in x(t)
  initial playout delay tradeoff: buffer starvation less likely with larger delay, but larger delay until user begins watching
variable fill
rate, x(t)
client application
buffer, size B
playout rate,
e.g., CBR r
buffer fill level, Q(t)
video server

## Slide 15: Streaming multimedia: UDP
server sends at rate appropriate for client
  often: send rate = encoding rate = constant rate
  transmission rate can be oblivious to congestion levels
short playout delay (2-5 seconds) to remove network jitter
error recovery: application-level
RTP [RFC 2326]: multimedia payload types
UDP may not go through firewalls

## Slide 16: Streaming multimedia: HTTP
multimedia file retrieved via HTTP GET
send at maximum possible rate under TCP
fill rate fluctuates due to TCP congestion control, retransmissions (in-order delivery)
larger playout delay: smooth TCP delivery rate
HTTP/TCP passes more easily through firewalls
variable rate, x(t)
TCP send buffer
video
file
TCP receive buffer
application playout buffer
server
client

## Slide 17: Multimedia networking: outline
9.1 multimedia networking applications
9.2 streaming stored video
9.3 voice-over-IP
9.4 protocols for real-time conversational applications
9.5 network support for multimedia

## Slide 18: Voice-over-IP (VoIP)
VoIP end-end-delay requirement: needed to maintain “conversational” aspect
  higher delays noticeable, impair interactivity
  < 150 msec: good
  > 400 msec bad
  includes application-level (packetization, playout), network delays
session initialization: how does callee advertise IP address, port number, encoding algorithms?
value-added services: call forwarding, screening, recording
emergency services: 911

## Slide 19: VoIP characteristics
speaker’s audio: alternating talk spurts, silent periods.
  64 kbps during talk spurt
  pkts generated only during talk spurts
  20 msec chunks at 8 Kbytes/sec: 160 bytes of data
application-layer header added to each chunk
chunk+header encapsulated into UDP or TCP segment
application sends segment into socket every 20 msec during talkspurt

## Slide 20: VoIP: packet loss, delay
network loss: IP datagram lost due to network congestion (router buffer overflow)
delay loss: IP datagram arrives too late for playout at receiver
  delays: processing, queueing in network; end-system (sender, receiver) delays
  typical maximum tolerable delay: 400 ms
loss tolerance: depending on voice encoding, loss concealment, packet loss rates between 1% and 10% can be tolerated

## Slide 21: Delay jitter
constant bit
rate
transmission
Cumulative data
time
variable
network
delay
(jitter)
client
reception
constant bit
rate playout
at client
client playout
delay
buffered
data
end-to-end delays of two consecutive packets: difference can be more or less than 20 msec (transmission time difference)

## Slide 22: VoIP: fixed playout delay
receiver attempts to playout each chunk exactly q msecs after chunk was generated.
  chunk has time stamp t: play out chunk at t+q
  chunk arrives after t+q: data arrives too late for playout: data “lost”
tradeoff in choosing q:
  large q: less packet loss
  small q: better interactive experience

## Slide 23: VoIP: fixed playout delay
sender generates packets every 20 msec during talk spurt.
first packet received at time r
first playout schedule: begins at p
second playout schedule: begins at p’

## Slide 24: Adaptive playout delay (1)
goal: low playout delay, low late loss rate
approach: adaptive playout delay adjustment:
  estimate network delay, adjust playout delay at beginning of each talk spurt
  silent periods compressed and elongated
  chunks still played out every 20 msec during talk spurt
adaptively estimate packet delay: (EWMA - exponentially weighted moving average, recall TCP RTT estimate):
di = (1-a)di-1 + a (ri – ti)
delay estimate after ith packet
small constant, e.g. 0.1
time received -
time sent (timestamp)
measured delay of ith packet

## Slide 25: Adaptive playout delay (2)
also useful to estimate average deviation of delay, vi :
estimates di, vi calculated for every received packet, but used only at start of talk spurt
for first packet in talk spurt, playout time is:
remaining packets in talkspurt are played out periodically
vi = (1-b)vi-1 + b |ri – ti – di|
playout-timei = ti + di + Kvi

## Slide 26: Adaptive playout delay (3)
Q: How does receiver determine whether packet is first in a talkspurt?
if no loss, receiver looks at successive timestamps
  difference of successive stamps > 20 msec -->talk spurt begins.
with loss possible, receiver must look at both time stamps and sequence numbers
  difference of successive stamps > 20 msec and sequence numbers without gaps --> talk spurt begins.

## Slide 27: VoiP: recovery from packet loss (1)
Challenge: recover from packet loss given small tolerable delay between original transmission and playout
each ACK/NAK takes ~ one RTT
alternative: Forward Error Correction (FEC)
  send enough bits to allow recovery without retransmission (recall two-dimensional parity in Ch. 5)
simple FEC
for every group of n chunks, create redundant chunk by exclusive OR-ing n original chunks
send n+1 chunks, increasing bandwidth by factor 1/n
can reconstruct original n chunks if at most one lost chunk from n+1 chunks, with playout delay

## Slide 28: VoiP: recovery from packet loss (2)
another FEC scheme:
“piggyback lower quality stream”
send lower resolution audio stream as redundant information
e.g., nominal stream PCM at 64 kbps and redundant stream GSM at 13 kbps
non-consecutive loss: receiver can conceal loss
generalization: can also append (n-1)st and (n-2)nd low-bit rate chunk

## Slide 29: VoiP: recovery from packet loss (3)
interleaving to conceal loss:
audio chunks divided into smaller units, e.g. four 5 msec units per 20 msec audio chunk
packet contains small units from different chunks
if packet lost, still have most of every original chunk
no redundancy overhead, but increases playout delay

## Slide 30: Voice-over-IP: Skype
supernode
overlay
network
proprietary application-layer protocol (inferred via reverse engineering)
  encrypted msgs
P2P components:
Skype clients (SC)
  clients: Skype peers connect directly to each other for VoIP call
  super nodes (SN): Skype peers with special functions
  overlay network: among SNs to locate SCs
  login server
Skype
login server
supernode (SN)

## Slide 31: P2P voice-over-IP: Skype
Skype client operation:
1. joins Skype network by contacting SN (IP address cached) using TCP
2. logs-in (username, password) to centralized Skype login server
3. obtains IP address for callee from SN, SN overlay
  or client buddy list
4. initiate call directly to callee
Skype
login server

## Slide 32: Skype: peers as relays
problem: both Alice, Bob are behind “NATs”
  NAT prevents outside peer from initiating connection to insider peer
  inside peer can initiate connection to outside
relay solution: Alice, Bob maintain open connection
to their SNs
  Alice signals her SN to connect to Bob
  Alice’s SN connects to Bob’s SN
  Bob’s SN connects to Bob over open connection Bob initially initiated to his SN

## Slide 33: Multimedia networking: outline
9.1 multimedia networking applications
9.2 streaming stored video
9.3 voice-over-IP
9.4 protocols for real-time conversational applications: RTP, SIP
9.5 network support for multimedia

## Slide 34: Real-Time Protocol (RTP)
RTP specifies packet structure for packets carrying audio, video data
RFC 3550
RTP packet provides
  payload type identification
  packet sequence numbering
  time stamping
RTP runs in end systems
RTP packets encapsulated in UDP segments
interoperability: if two VoIP applications run RTP, they may be able to work together

## Slide 35: RTP runs on top of UDP
RTP libraries provide transport-layer interface
that extends UDP:
  port numbers, IP addresses
  payload type identification
  packet sequence numbering
  time-stamping

## Slide 36: RTP example
example: sending 64 kbps PCM-encoded voice over RTP
application collects encoded data in chunks, e.g., every 20 msec = 160 bytes in a chunk
audio chunk + RTP header form RTP packet, which is encapsulated in UDP segment
RTP header indicates type of audio encoding in each packet
  sender can change encoding during conference
RTP header also contains sequence numbers, timestamps

## Slide 37: RTP and QoS
RTP does not provide any mechanism to ensure timely data delivery or other QoS guarantees
RTP encapsulation only seen at end systems (not by intermediate routers)
  routers provide best-effort service, making no special effort to ensure that RTP packets arrive at destination in timely matter

## Slide 38: RTP header
payload type (7 bits): indicates type of encoding currently being used. If sender changes encoding during call, sender
informs receiver via payload type field
  Payload type 0: PCM mu-law, 64 kbps
  Payload type 3: GSM, 13 kbps
  Payload type 7: LPC, 2.4 kbps
  Payload type 26: Motion JPEG
  Payload type 31: H.261
  Payload type 33: MPEG2 video
sequence # (16 bits): increment by one for each RTP packet sent
  detect packet loss, restore packet sequence
payload type
sequence number type
time stamp
Synchronization
Source ID
Miscellaneous fields

## Slide 39: RTP header
timestamp field (32 bits long): sampling instant of first byte in this RTP data packet
  for audio, timestamp clock increments by one for each sampling period (e.g., each 125 usecs for 8 KHz sampling clock)
  if application generates chunks of 160 encoded samples, timestamp increases by 160 for each RTP packet when source is active. Timestamp clock continues to increase at constant rate when source is inactive.
SSRC field (32 bits long): identifies source of RTP stream. Each stream in RTP session has distinct SSRC
payload type
sequence number type
time stamp
Synchronization
Source ID
Miscellaneous fields

## Slide 40: RTSP/RTP programming assignment
build a server that encapsulates stored video frames into RTP packets
  grab video frame, add RTP headers, create UDP segments, send segments to UDP socket
  include seq numbers and time stamps
  client RTP provided for you
also write client side of RTSP
  issue play/pause commands
  server RTSP provided for you

## Slide 41: Real-Time Control Protocol (RTCP)
works in conjunction with RTP
each participant in RTP session periodically sends RTCP control packets to all other participants
each RTCP packet contains sender and/or receiver reports
  report statistics useful to application: # packets sent, # packets lost, interarrival jitter
feedback used to control performance
  sender may modify its transmissions based on feedback

## Slide 42: RTCP: multiple multicast senders
each RTP session: typically a single multicast address; all RTP /RTCP packets belonging to session use multicast address
RTP, RTCP packets distinguished from each other via distinct port numbers
to limit traffic, each participant reduces RTCP traffic as number of conference participants increases
RTCP
RTP
RTCP
RTCP
sender
receivers

## Slide 43: RTCP: packet types
receiver report packets:
fraction of packets lost, last sequence number, average interarrival jitter
sender report packets:
SSRC of RTP stream, current time, number of packets sent, number of bytes sent
source description packets:
e-mail address of sender, sender's name, SSRC of associated RTP stream
provide mapping between the SSRC and the user/host name

## Slide 44: RTCP: stream synchronization
RTCP can synchronize different media streams within a RTP session
e.g., videoconferencing app: each sender generates one RTP stream for video, one for audio.
timestamps in RTP packets tied to the video, audio sampling clocks
  not tied to wall-clock time
each RTCP sender-report packet contains (for most recently generated packet in associated RTP stream):
  timestamp of RTP packet
  wall-clock time for when packet was created
receivers uses association to synchronize playout of audio, video

## Slide 45: RTCP: bandwidth scaling
RTCP attempts to limit its traffic to 5% of session bandwidth
example : one sender, sending video at 2 Mbps
RTCP attempts to limit RTCP traffic to 100 Kbps
RTCP gives 75% of rate to receivers; remaining 25% to sender
75 kbps is equally shared among receivers:
  with R receivers, each receiver gets to send RTCP traffic at 75/R kbps.
sender gets to send RTCP traffic at 25 kbps.
participant determines RTCP packet transmission period by calculating avg RTCP packet size (across entire session) and dividing by allocated rate

## Slide 46: SIP: Session Initiation Protocol [RFC 3261]
long-term vision:
all telephone calls, video conference calls take place over Internet
people identified by names or e-mail addresses, rather than by phone numbers
can reach callee (if callee so desires), no matter where callee roams, no matter what IP device callee is currently using

## Slide 47: SIP services
SIP provides mechanisms for call setup:
  for caller to let callee know she wants to establish a call
  so caller, callee can agree on media type, encoding
  to end call
determine current IP address of callee:
  maps mnemonic identifier to current IP address
call management:
  add new media streams during call
  change encoding during call
  invite others
  transfer, hold calls

## Slide 48: Example: setting up call to known IP address
Alice’s SIP invite message indicates her port number, IP address, encoding she prefers to receive (PCM mlaw)
Bob’s 200 OK message indicates his port number, IP address, preferred encoding (GSM)
SIP messages can be sent over TCP or UDP; here sent over RTP/UDP
default SIP port number is 5060

## Slide 49: Setting up a call (more)
codec negotiation:
  suppose Bob doesn’t have PCM mlaw encoder
  Bob will instead reply with 606 Not Acceptable Reply, listing his encoders. Alice can then send new INVITE message, advertising different encoder
rejecting a call
  Bob can reject with replies “busy,” “gone,” “payment required,” “forbidden”
media can be sent over RTP or some other protocol

## Slide 50: Example of SIP message
INVITE sip:bob@domain.com SIP/2.0
Via: SIP/2.0/UDP 167.180.112.24
From: sip:alice@hereway.com
To: sip:bob@domain.com
Call-ID: a2e3a@pigeon.hereway.com
Content-Type: application/sdp
Content-Length: 885
c=IN IP4 167.180.112.24
m=audio 38060 RTP/AVP 0
Notes:
HTTP message syntax
sdp = session description protocol
Call-ID is unique for every call
Here we don’t know Bob’s IP address
  intermediate SIP servers needed
Alice sends, receives SIP messages using SIP default port 506
Alice specifies in header that SIP client sends, receives SIP messages over UDP

## Slide 51: Name translation, user location
caller wants to call callee, but only has callee’s name or e-mail address.
need to get IP address of callee’s current host:
  user moves around
  DHCP protocol
  user has different IP devices (PC, smartphone, car device)
result can be based on:
  time of day (work, home)
  caller (don’t want boss to call you at home)
  status of callee (calls sent to voicemail when callee is already talking to someone)

## Slide 52: SIP registrar
REGISTER sip:domain.com SIP/2.0
Via: SIP/2.0/UDP 193.64.210.89
From: sip:bob@domain.com
To: sip:bob@domain.com
Expires: 3600
one function of SIP server: registrar
when Bob starts SIP client, client sends SIP REGISTER message to Bob’s registrar server
register message:

## Slide 53: SIP proxy
another function of SIP server: proxy
Alice sends invite message to her proxy server
  contains address sip:bob@domain.com
  proxy responsible for routing SIP messages to callee, possibly through multiple proxies
Bob sends response back through same set of SIP proxies
proxy returns Bob’s SIP response message to Alice
  contains Bob’s IP address
SIP proxy analogous to local DNS server plus TCP setup

## Slide 54: SIP example: jim@umass.edu calls keith@poly.edu
1
1. Jim sends INVITE message to UMass SIP proxy.
2. UMass proxy forwards request
to Poly registrar server
2
3. Poly server returns redirect response, indicating that it should try keith@eurecom.fr
3
5. eurecom registrar forwards INVITE to 197.87.54.21, which is running keith’s SIP client
5
4
4. Umass proxy forwards request
to Eurecom registrar server
8
6
7
6-8. SIP response returned to Jim
9
9. Data flows between clients
UMass SIP proxy
Poly SIP
registrar
Eurecom SIP
registrar
197.87.54.21
128.119.40.186

## Slide 55: Comparison with H.323
H.323: another signaling protocol for real-time, interactive multimedia
H.323: complete, vertically integrated suite of protocols for multimedia conferencing: signaling, registration, admission control, transport, codecs
SIP: single component. Works with RTP, but does not mandate it. Can be combined with other protocols, services
H.323 comes from the ITU (telephony)
SIP comes from IETF: borrows much of its concepts from HTTP
  SIP has Web flavor; H.323 has telephony flavor
SIP uses KISS principle: Keep It Simple Stupid

## Slide 56: Multimedia networking: outline
9.1 multimedia networking applications
9.2 streaming stored video
9.3 voice-over-IP
9.4 protocols for real-time conversational applications
9.5 network support for multimedia

## Slide 57: Network support for multimedia

## Slide 58: Dimensioning best effort networks
approach: deploy enough link capacity so that congestion doesn’t occur, multimedia traffic flows without delay or loss
  low complexity of network mechanisms (use current “best effort” network)
  high bandwidth costs
challenges:
  network dimensioning: how much bandwidth is “enough?”
  estimating network traffic demand: needed to determine how much bandwidth is “enough” (for that much traffic)

## Slide 59: Providing multiple classes of service
thus far: making the best of best effort service
  one-size fits all service model
alternative: multiple classes of service
  partition traffic into classes
  network treats different classes of traffic differently (analogy: VIP service versus regular service)
0111
granularity: differential service among multiple classes, not among individual connections
history: ToS bits

## Slide 60: Multiple classes of service: scenario
R1
R2
H1
H2
H3
H4
1.5 Mbps link
R1 output
interface
queue

## Slide 61: Scenario 1: mixed HTTP and VoIP
example: 1Mbps VoIP, HTTP share 1.5 Mbps link.
  HTTP bursts can congest router, cause audio loss
  want to give priority to audio over HTTP
packet marking needed for router to distinguish between different classes; and new router policy to treat packets accordingly
Principle 1
R1
R2

## Slide 62: Principles for QOS guarantees (more)
what if applications misbehave (VoIP sends higher than declared rate)
  policing: force source adherence to bandwidth allocations
marking, policing at network edge
provide protection (isolation) for one class from others
Principle 2
R1
R2
1.5 Mbps link
1 Mbps
phone
packet marking and policing

## Slide 63: Principles for QOS guarantees (more)
allocating fixed (non-sharable) bandwidth to flow: inefficient use of bandwidth if flows doesn’t use its allocation
while providing isolation, it is desirable to use
resources as efficiently as possible
Principle 3
R1
R2
1.5 Mbps link
1 Mbps
phone
1 Mbps logical link
0.5 Mbps logical link

## Slide 64: Scheduling and policing mechanisms
packet scheduling: choose next queued packet to send on outgoing link
previously covered in Chapter 4:
  FCFS: first come first served
  simply multi-class priority
  round robin
  weighted fair queueing (WFQ)
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)

## Slide 65: Policing mechanisms
goal: limit traffic to not exceed declared parameters
Three common-used criteria:
(long term) average rate: how many pkts can be sent per unit time (in the long run)
  crucial question: what is the interval length: 100 packets per sec or 6000 packets per min have same average!
peak rate: e.g., 6000 pkts per min (ppm) avg.; 1500 ppm peak rate
(max.) burst size: max number of pkts sent consecutively (with no intervening idle)

## Slide 66: Policing mechanisms: implementation
token bucket: limit input to specified burst size and average rate
bucket can hold b tokens
tokens generated at rate r token/sec unless bucket full
over interval of length t: number of packets admitted less than or equal to (r t + b)

## Slide 67: Policing and QoS guarantees
token bucket, WFQ combine to provide guaranteed upper bound on delay, i.e., QoS guarantee!
WFQ
token rate, r
bucket size, b
per-flow
rate, R
D = b/R
max
arriving
traffic
arriving
traffic

## Slide 68: Differentiated services
want “qualitative” service classes
  “behaves like a wire”
  relative service distinction: Platinum, Gold, Silver
scalability: simple functions in network core, relatively complex functions at edge routers (or hosts)
  signaling, maintaining per-flow router state difficult with large number of flows
don’t define define service classes, provide functional components to build service classes

## Slide 69: Diffserv architecture
edge router:
per-flow traffic management
marks packets as in-profile and out-profile
core router:
per class traffic management
buffering and scheduling based on marking at edge
preference given to in-profile packets over out-of-profile packets
r
b
marking
scheduling
.
.
.

## Slide 70
Edge-router packet marking
class-based marking: packets of different classes marked differently
intra-class marking: conforming portion of flow marked differently than non-conforming one
profile: pre-negotiated rate r, bucket size b
packet marking at edge based on per-flow profile
possible use of marking:
user packets
rate r
b

## Slide 71: Diffserv packet marking: details
packet is marked in the Type of Service (TOS) in IPv4, and Traffic Class in IPv6
6 bits used for Differentiated Service Code Point (DSCP)
  determine PHB that the packet will receive
  2 bits currently unused
DSCP
unused

## Slide 72: Classification, conditioning
may be desirable to limit traffic injection rate of some class:
user declares traffic profile (e.g., rate, burst size)
traffic metered, shaped if non-conforming

## Slide 73: Forwarding Per-hop Behavior (PHB)
PHB result in a different observable (measurable) forwarding performance behavior
PHB does not specify what mechanisms to use to ensure required PHB performance behavior
examples:
  class A gets x% of outgoing link bandwidth over time intervals of a specified length
  class A packets leave first before packets from class B

## Slide 74: Forwarding PHB
PHBs proposed:
expedited forwarding: packet departure rate of a class equals or exceeds specified rate
  logical link with a minimum guaranteed rate
assured forwarding: 4 classes of traffic
  each guaranteed minimum amount of bandwidth
  each with three drop preference partitions

## Slide 75: Per-connection QOS guarantees
basic fact of life: can not support traffic demands beyond link capacity
call admission: flow declares its needs, network may
block call (e.g., busy signal) if it cannot meet needs
Principle 4
R1
R2
1.5 Mbps link
1 Mbps
phone
1 Mbps
phone

## Slide 76: QoS guarantee scenario
resource reservation
  call setup, signaling (RSVP)
  traffic, QoS declaration
  per-element admission control
  QoS-sensitive scheduling (e.g., WFQ)
request/
reply

## Slide 77: Multimedia networking: outline
9.1 multimedia networking applications
9.2 streaming stored video
9.3 voice-over-IP
9.4 protocols for real-time conversational applications
9.5 network support for multimedia

## Slide 78: Q & A